## Slide 1: Computer Organization
COIS 2300H
Brian Srivastava

## Slide 2: Close to the Metal
This course is very much the hardware software boundary
Hardware components provide software instructions (e.g. add, matrix multiply, divide etc.)
High level languages get translated into low level languages to be run, but how does that happen?
Can an instruction set be efficient (however you want to define it)?
Notes: Stealing a slogan from AMD/ATI

## Slide 3: Measuring performance
In 2020H you are worried about questions like ‘what is the most efficient way to search N things’
In 2300H you are worried about questions like ‘what is the most efficient way to store a number in memory’ or how to multiply two integers/floating point/etc. numbers together

## Slide 4: Simple math
c=a*b, c=a+b, c=a/b (for example).
Will ints and floats have different speeds?
What about 8/16/32/64 bits length?
If, at 1Hz (or realistically 1GHz) processor A can do 300 million c=a*b a second, and Processor B (say, a never version of A) can do 330 million what does that mean?

## Slide 5: Cherry Picking Some Data
There’s lots wrong with the technique here, in part the
Author didn’t optimise their code properly… and got these results
Useful to know what happens when you do things wrong
(including use bad compiler options).
Notes: http://nicolas.limare.net/pro/notes/2014/12/12_arit_speed/ - note the clocks aren’t the same so it’s not 1:1

## Slide 6: Digital Logic
This course builds on digital logic (bottom up)*
But this course also builds on 1020 (top down)
* N.B. The reverse is sort of also true, in digital logic you learn to make things but without context have no idea how they’re useful

## Slide 7: TextBook
Buy it
Yes really
Sorry
(And by buy, I mean the PDF version is fine)

## Slide 8: Book
There are I think two versions of the same book
We want the MIPS version NOT the RISC-V version (I might adopt that in future but not this year, no time, not that it matters much)

## Slide 9: Mars
The book comes with a program called Mars
(MIPS assembler and Runtime Simulator)
MIPS is a fake(sort of) assembly language, it’s pretty much the standard one people actually use for teaching
Unfortunately Mars runs on java. So you need to have java installed.
http://courses.missouristate.edu/KenVollmar/mars/download.htm
https://www.java.com/en/

## Slide 10: Java
Java is horrible, I know, sorry.
Always install java updates, if it breaks Mars, well then we’ll find another plan.
DO NOT LEAVE UNPATCHED JAVA RUNNING ON YOUR MACHINE

## Slide 11: 4k vs 1080
Oh and Mars sucks at 4k unless you use Java 9
It works, it’s just that the menu’s and text are absurdly tiny.

## Slide 12: Evaluations
Note, these dates may get moved back a bit (not the mid term), because it might be tricky to do everything you need to on time for A1 and A2.
Labs are due one week after the lab
Type of Assignment | Weighting | Due Date
Labs (10 of 12) | 10 | Weekly
Assignment 1 | 10 | Jan 24
Assignment 2 | 10 | Feb 14
Midterm Examination | 20 | Feb 25 in Class
Assignment 3 | 10 | March 17
Assignment 4 | 10 | April 6th
Final Examination | 30 | TBA

## Slide 13: Academic Integrity
Academic Integrity: Academic dishonesty, which includes plagiarism and cheating, is an extremely serious academic offence and carries penalties varying from a 0 grade on an assignment to expulsion from the University. Definitions, penalties, and procedures for dealing with plagiarism and cheating are set out in Trent University’s Academic Integrity Policy. You have a responsibility to educate yourself – unfamiliarity with the policy is not an excuse. You are strongly encouraged to visit Trent’s Academic Integrity website to learn more: www.trentu.ca/academicintegrity.

## Slide 14: Lateness (Officially)…
Lateness: 10% per business day (i.e. any time on Saturday, Sunday or Monday will all be the same one day 10% late). Assignments will not be accepted if they are more than one week late. Extensions are possible if there is an emergency, or through arrangement with the instructor in advance. Appropriate documentation supporting extensions is required (e.g. note from medical practitioner, SAS Office, or Counselling Centre). Due dates will be adjusted if there are technical problems with Blackboard or labs providing support for the course.

## Slide 15: Religious Accommodation
Over the summer that needs to be arranged with the instructor
The regular term it’s about the 3rd week in class you need to inform the registrar.

## Slide 16: Access to Instruction
Access to Instruction: It is Trent University's intent to create an inclusive learning environment. If a student has a disability and documentation from a regulated health care practitioner and feels that he/she may need accommodations to succeed in a course, the student should contact the Student Accessibility Services Office (SAS) at the respective campus as soon as possible.

## Slide 17: Course Outline
Lecture Topic | Lab topic
Introduction | Intro To MIPS and MARS
Assembly Programming (introduction) | , mips instructions
Arithmetic for computers | first MIPS program that does anything
Logical Design of a Processor | Procedure calls, recursion
Memory Hierarchy (cache) | Arithmetic
Mid Term | 
Storage (RAM and Disk) | Compiling to ASM, x86 (just a little)
Multicore processors | Profiling, Tracing
Review | 
Notes: LEARN BINARY DECIMAL CONVERSIONS

## Slide 18: MIPS, x86
MIPS is a Reduced instruction set system. (Meaning there aren’t that many instructions)
We run in a simulated environment
X86 Assembler – well, Intel assembly, is run using MASM as part of visual studio or GCC – GCC just added a new option (by just I mean last week) that might make this easier, so we’ll look into that later.
Debugging actual x86 code is frustratingly difficult, even getting it up and running is frustratingly difficult. So we’ll save that for later

## Slide 19: ARM
ARM shows up two places, mobile devices and their derivatives in the CPU business
And Raspberry Pi
Actually doing assembly programming on a pi is a nightmare if it ever works, so I don’t recommend you try.

## Slide 20: Workshops/Labs
The plan (at the moment) is that for several of them we’ll do something like tutorials/programming labs
So lab this week we’ll do assembly programming IDE
During lab I’ll expect you to talk with your friends in class and so on.

## Slide 21: Labs
You need a laptop. Or maybe not.
The ATOP lab is up and running

## Slide 22: Chapter 1
Computer Abstractions and Technology

## Slide 23: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive
§1.1 Introduction

## Slide 24: Classes of Computers
Personal computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized

## Slide 25: Classes of Computers
Supercomputers
  High-end scientific and engineering calculations
  Highest capability but represent a small fraction of the overall computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints

## Slide 26: The PostPC Era

## Slide 27: Tablet vs Slate
Note that the book uses the term “tablet” when it means “slate”
That has become the public convention because of the iPad, but more correctly it’s a slate.

## Slide 28: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google

## Slide 29: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing

## Slide 30: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 31: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy
§1.2 Eight Great Ideas in Computer Architecture

## Slide 32: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.3 Below Your Program

## Slide 33: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 34: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.4 Under the Covers
The BIG Picture

## Slide 35: Touchscreen
PostPC device
Supersedes keyboard and mouse
Resistive and Capacitive types
  Most tablets, smart phones use capacitive
  Capacitive allows multiple touches simultaneously

## Slide 36
https://www.youtube.com/watch?v=9BnLbv6QYcA

## Slide 37: Through the Looking Glass
LCD screen: picture elements (pixels)
  Mirrors content of frame buffer memory

## Slide 38: Opening the Box
Capacitive multitouch LCD screen
3.8 V, 25 Watt-hour battery
Computer board

## Slide 39: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 40: Inside the Processor
Apple A5
Notes: GPIO means general purpose input output (USB or in the case of apple, thunderbolt connectors)
Data paths are a collection of parts that do something (Usually a computing task) along with memory and so on. In this case the A5 is a dual ARM cortex A9 cpu, and a dual core PowerVR SGX543MP2 GPU.

## Slide 41: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface
The BIG Picture

## Slide 42: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 43: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 44: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity
§1.5 Technologies for Building Processors and Memory

## Slide 45: Semiconductor Technology
Silicon: semiconductor
Add materials to transform properties:
  Conductors
  Insulators
  Switch

## Slide 46: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 47: Intel Core i7 Wafer
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm

## Slide 48: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 49: Contracts
Intel (and sometimes Samsung) makes their own stuff
Everyone else buys from someone else (fabless, and fabs)
Some companies buy/sell wafers, others sell completed dies
Notes: Sri note

## Slide 50: Node Size
For want of a better way of putting it this usually measured in nm (today) or m in the 1970’s
In ~2021 5nm will likely be the last (or close there to) semiconductor node using silicon
After that we might be able to use graphene down to 1nm
And then we’re boned
Notes: Sri addition

## Slide 51: Node Size Ctd
Think of a transistor has having it’s dimensions as being node size basically
So 5nm is twice the density of 7nm (roughly, 25nm2 to 49nm2)
The problem is that at the current 14/16 nodes TSMC and Globalfoundries have started talking about the shortest side, not the average size, which is confusing
Notes: Sri addition

## Slide 52: Defining Performance
Which airplane has the best performance?
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Passenger Capacity | 146 | 132 | 470 | 375
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Range (miles) | 8720 | 4000 | 4150 | 4630
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Speed (mph) | 544 | 1350 | 610 | 610
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Passengers x mph | 79424 | 178200 | 286700 | 228750
§1.6 Performance

## Slide 53: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 54: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 55: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 56: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 57: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 58: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 59: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 60: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 61: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 62: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 63: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 64: Power Trends
In CMOS IC technology
§1.7 The Power Wall
×1000
×30
5V → 1V

## Slide 65: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 66: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 67: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 68: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)

## Slide 69: CINT2006 for Intel Core i7 920

## Slide 70: SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)

## Slide 71: SPECpower_ssj2008 for Xeon X5650

## Slide 72: SPEC
SPEC isn’t particularly well regarded in the CPU benchmarking community it is good for comparing different architectures to each other but otherwise is pretty bad

## Slide 73: Apple A9 vs Intel
Notes: http://www.anandtech.com/show/9766/the-apple-ipad-pro-review/4

## Slide 74: The M 5Y71
The Core M 5Y71 is a 4.5 Watt processor
The A9 is about the same (3.5-4 as best I can tell)
These are a long way from the good CPU’s that can draw 200W and are easily a factor of 7 more powerful
(note that good CPU’s don’t integrate GPU’s which the M line and A9 do, so again, different products)
Notes: http://ark.intel.com/products/84672/Intel-Core-M-5Y71-Processor-4M-Cache-up-to-2_90-GHz

## Slide 75: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?
Corollary: make the common case fast

## Slide 76: Fallacy: Low Power at Idle
Look back at i7 power benchmark
  At 100% load: 258W
  At 50% load: 170W (66%)
  At 10% load: 121W (47%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load

## Slide 77: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU

## Slide 78: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks