## Slide 1: Chapter 6
Parallel Processors from Client to Cloud

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Task-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)
§6.1 Introduction

## Slide 3: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., quad-core Xeon e5345
Software
  Sequential: e.g., matrix multiplication
  Concurrent: e.g., operating system
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 4: What We’ve Already Covered
§2.11: Parallelism and Instructions
  Synchronization
§3.6: Parallelism and Computer Arithmetic
  Subword Parallelism
§4.10: Parallelism and Advanced Instruction-Level Parallelism
§5.10: Parallelism and Memory Hierarchies
  Cache Coherence

## Slide 5: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs

## Slide 6: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90× speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time

## Slide 7: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors

## Slide 8: Scaling Example (cont)
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 9: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example

## Slide 10: Instruction and Data Streams
An alternate classification
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 11: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu r4,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,r4,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result

## Slide 12: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth

## Slide 13: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 14: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications

## Slide 15: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units:

## Slide 16: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
§6.4 Hardware Multithreading

## Slide 17: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches

## Slide 18: Multithreading Example

## Slide 19: Future of Multithreading
Will it survive? In what form?
Power considerations  simplified microarchitectures
  Simpler forms of multithreading
Tolerating cache-miss latency
  Thread switch may be most effective
Multiple simple cores might share resources more effectively

## Slide 20: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors

## Slide 21: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor
  sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 22: Example: Sum Reduction
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);

## Slide 23: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers (e.g., SGI)
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization
§6.6 Introduction to Graphics Processing Units

## Slide 24: Graphics in the System

## Slide 25: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 26: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 27: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 28: Classifying GPUs
Don’t fit nicely into SIMD/MIMD model
  Conditional execution in a thread allows an illusion of MIMD
    But with performance degredation
    Need to write general purpose code with care
 | Static: Discovered at Compile Time | Dynamic: Discovered at Runtime
Instruction-Level Parallelism | VLIW | Superscalar
Data-Level Parallelism | SIMD or Vector | Tesla Multiprocessor

## Slide 29: GPU Memory Structures

## Slide 30: Putting GPUs into Perspective
Feature | Multicore with SIMD | GPU
SIMD processors | 4 to 8 | 8 to 16
SIMD lanes/processor | 2 to 4 | 8 to 16
Multithreading hardware support for SIMD threads | 2 to 4 | 16 to 32
Typical ratio of single precision to double-precision performance | 2:1 | 2:1
Largest cache size | 8 MB | 0.75 MB
Size of memory address | 64-bit | 64-bit
Size of main memory | 8 GB to 256 GB | 4 GB to 6 GB
Memory protection at level of page | Yes | Yes
Demand paging | Yes | No
Integrated scalar processor/SIMD processor | Yes | No
Cache coherent | Yes | No

## Slide 31: Guide to GPU Terms

## Slide 32: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters, WSC, and Other Message-Passing MPs

## Slide 33: Loosely Coupled Clusters
Network of independent computers
  Each has private memory and OS
  Connected using I/O system
    E.g., Ethernet/switch, Internet
Suitable for applications with independent tasks
  Web servers, databases, simulations, …
High availability, scalable, affordable
Problems
  Administration cost (prefer virtual machines)
  Low interconnect bandwidth
    c.f. processor/memory bandwidth on an SMP

## Slide 34: Sum Reduction (Again)
Sum 100,000 on 100 processors
First distribute 100 numbers to each
  The do partial sums
  sum = 0; for (i = 0; i<1000; i = i + 1) sum = sum + AN[i];
Reduction
  Half the processors send, other half receive and add
  The quarter send, quarter receive and add, …

## Slide 35: Sum Reduction (Again)
Given send() and receive() operations
  limit = 100; half = 100;/* 100 processors */ repeat half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ until (half == 1); /* exit with final sum */
  Send/receive also provide synchronization
  Assumes send/receive take similar time to addition

## Slide 36: Grid Computing
Separate computers interconnected by long-haul networks
  E.g., Internet connections
  Work units farmed out, results sent back
Can make use of idle time on PCs
  E.g., SETI@home, World Community Grid

## Slide 37: Interconnection Networks
Network topologies
  Arrangements of processors, switches, and links
§6.8 Introduction to Multiprocessor Network Topologies
Bus
Ring
2D Mesh
N-cube (N = 3)
Fully connected

## Slide 38: Multistage Networks

## Slide 39: Network Characteristics
Performance
  Latency per message (unloaded network)
  Throughput
    Link bandwidth
    Total network bandwidth
    Bisection bandwidth
  Congestion delays (depending on traffic)
Cost
Power
Routability in silicon

## Slide 40: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models

## Slide 41: Code or Applications?
Traditional benchmarks
  Fixed code and data sets
Parallel programming is evolving
  Should algorithms, programming languages, and tools be part of the system?
  Compare systems, provided they implement a given application
  E.g., Linpack, Berkeley Design Patterns
Would foster innovation in approaches to parallelism

## Slide 42: Modeling Performance
Assume performance metric of interest is achievable GFLOPs/sec
  Measured using computational kernels from Berkeley Design Patterns
Arithmetic intensity of a kernel
  FLOPs per byte of memory accessed
For a given computer, determine
  Peak GFLOPS (from data sheet)
  Peak memory bytes/sec (using Stream benchmark)

## Slide 43: Roofline Diagram
Attainable GPLOPs/sec
= Max ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )

## Slide 44: Comparing Systems
Example: Opteron X2 vs. Opteron X4
  2-core vs. 4-core, 2× FP performance/core, 2.2GHz vs. 2.3GHz
  Same memory system
To get higher performance on X4 than X2
  Need high arithmetic intensity
  Or working set must fit in X4’s 2MB L-3 cache

## Slide 45: Optimizing Performance
Optimize FP performance
  Balance adds & multiplies
  Improve superscalar ILP and use of SIMD instructions
Optimize memory usage
  Software prefetch
    Avoid load stalls
  Memory affinity
    Avoid non-local data accesses

## Slide 46: Optimizing Performance
Choice of optimization depends on arithmetic intensity of code
Arithmetic intensity is not always fixed
  May scale with problem size
  Caching reduces memory accesses
    Increases arithmetic intensity

## Slide 47: i7-960 vs. NVIDIA Tesla 280/480
§6.11 Real Stuff: Benchmarking and Rooflines i7 vs. Tesla

## Slide 48: Rooflines

## Slide 49: Benchmarks

## Slide 50: Performance Summary
GPU (480) has 4.4 X the memory bandwidth
  Benefits memory bound kernels
GPU has 13.1 X the single precision throughout, 2.5 X the double precision throughput
  Benefits FP compute bound kernels
CPU cache prevents some kernels from becoming memory bound when they otherwise would on GPU
GPUs offer scatter-gather, which assists with kernels with strided data
Lack of synchronization and memory consistency support on GPU limits performance for some kernels

## Slide 51: Multi-threading DGEMM
§6.12 Going Faster: Multiple Processors and Matrix Multiply
Use OpenMP:
void dgemm (int n, double* A, double* B, double* C)
{
#pragma omp parallel for
for ( int sj = 0; sj < n; sj += BLOCKSIZE )
for ( int si = 0; si < n; si += BLOCKSIZE )
for ( int sk = 0; sk < n; sk += BLOCKSIZE )
do_block(n, si, sj, sk, A, B, C);
}

## Slide 52: Multithreaded DGEMM

## Slide 53: Multithreaded DGEMM

## Slide 54: Fallacies
Amdahl’s Law doesn’t apply to parallel computers
  Since we can achieve linear speedup
  But only on applications with weak scaling
Peak performance tracks observed performance
  Marketers like this approach!
  But compare Xeon with others in example
  Need to be aware of bottlenecks
§6.13 Fallacies and Pitfalls

## Slide 55: Pitfalls
Not developing the software to take account of a multiprocessor architecture
  Example: using a single lock for a shared composite resource
    Serializes accesses, even if they could be done in parallel
    Use finer-granularity locking

## Slide 56: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
SaaS importance is growing and clusters are a good match
Performance per dollar and performance per Joule drive both mobile and WSC
§6.14 Concluding Remarks

## Slide 57: Concluding Remarks (con’t)
SIMD and vector operations match multimedia applications and are easy to program